Installation Guide

1-Completly clean out gutter system            2-Inspect miters for possible leaks

3-Reseal miter if needed                            4-Check hangers for tightness

5-Mark 45° line on Leaf Solution                   6-Cut off angled piece

7-Snip channels from bottom                       8-Bend at a 90 to aid cutting

9-Cut off angled piece                             10-repeat for other side

11- Remove and save old splash guard        12-Make two-2”x8” fins

13-insert fin in center channel                  14-Line up fin with angled edge

15-run zip screws through channel/fin        16-Finished fin installed-repeat

17-lift valley tin and slide panel under         18-Slide panel flush with miter corner

19-Screw panel to gutter                         20-line up panel and screw other end

21-install screw in center                          22-repeat with other half of miter

23-Push in holes at end of fins with an awl   24-detail of holes in rear of fin

25Ffins not needed for outside miters       26-Butt next piece against mitered piece

27-straighten piece along gutter              28-fasten with 3 zip screws

29- Repeat steps 26-28 to end of run      30-butt last panel against previous

31-Mark bend line just inside end-cap       32-Square bend line, leave 2” past line

33-Cut away front lip up to bend line        34-Notch mesh as shown

35-Notch rear of piece as shown             36-Finished view of notches

37-Bend notched area down 90°            38-Slide against inside of end cap, screw

39-Finished view of end cap                   40-Another angle view

41-View towards miter                            42-Finished view